INTERNATIONAL INDIAN SCHOOL, RIYADH

GRADE – XII			PHYSICS

FIRST TERM WORKSHEET – 2013 – 14

CH -1 Electric charge and Fields

- ‘Electric charge is quantized’. What is meant by this statement?

- Define the term electric dipole moment. Is it scalar or vector?

- Write the SI unit of electric flux.

- Why no two electric lines of force can intersect each other.

- Derive an expression for torque acting on an electric dipole in a uniform electric field.

- A proton and an electron are placed 1.6 cm apart in free space. Find the magnitude of electrostatic force between them. What is the nature of this force?

- Derive an expression for dipole field intensity at a point on the dipole axis.

- State Gauss’s theorem in electrostatics. Apply this theorem to derive an expression for electric field intensity at a point near an infinitely long straight charged wire.

- A conducting sphere of radius 10 cm has an unknown charge. If the electric field 20 cm from the center of the sphere is 1.5 x 103 N/C and points radially inwards, what is the net charge on the sphere?

Electromagnetic Induction and Alternating currents

- What are eddy currents? How can they be minimized?

- State the law that gives the polarity of induced emf.

- Define self inductance. Write its SI unit.

- How will the inductive reactance and capacitive reactance change on doubling the frequency of alternating current?

- Peak value of emf of an a.c source is Eo. What is its rms value?

- What is an impedance triangle?

- A wire of length 0.1m moves with a speed of 10 m/s perpendicular to a magnetic field of induction 1 Wb/m2. What is the value of induced emf?

- A current of 10 A in primary of a circuit is reduced to zero at a uniform rate in 10-3s of coefficient of mutual inductance is 3H, what is the induced emf in the secondary?

- Derive a expression for the coefficient of mutual inductance between two long solenoids.

- A transformer has an efficiency of 80%. It works at 4 kw and 100 volt. If the secondary voltage is 240 V, find the primary and secondary currents.

- Explain the construction and working of a.c generator.

- Show that average power consumed per cycle in an a.c circuit containing an ideal capacitor is zero.

- With the help of a suitable phasor diagram, obtain a relation for impedance in a series LCR circuit.

- Explain the term capacitative reactance. Show graphically the variation of capacitative reactance with frequency of alternating voltage.

- Define Q factor of the circuit.

Electromagnetic waves

- Name the electromagnetic waves in the order of increasing wavelength.

- Write two uses of X – rays.

- What do you mean by the transverse nature of electromagnetic waves?

- Define displacement current and get modified form of Ampere’s circuital law.

- Write uses of

- Infra red

- Gamma rays

- Radio waves

- Micro waves

- What is electromagnetic spectrum?

- Write the characteristics of electro magnetic waves.

Magnetic effect of current and magnetism

- State curie law in magnetism.

- Which materials have negative value of magnetic susceptibility?

- Which material is used in making permanent magnets and why?

- What is the direction of dipole moment?

- What is the angle of dip at a place where horizontal and vertical components of earths field are equal?

- What are magnetic elements at a place? Define them.

- Describe construction, theory and working of a tangent galvanometer.

- What is a cyclotron? Discuss its construction, working and theory.

- A short bar magnet placed with its axis at 30o with a uniform external magnetic field of 0.15 T experiences a torque of magnitude equal to 4.5 x 10-2  J. what is the magnitude of magnetic moment of the magnet?

- A horizontal overhead power line carries a current of 90A in east to west direction. What is the magnitude and direction of the magnetic field due to the current 1.5m below the line?

Ch 2 Electric potential and capacitance

- The electric potential V is constant in a region. What can you say about the electric field there?

- Draw an equipotential surface for a uniform electric field?

- Sketch a graph to how charge Q given to a capacitor of capacity C varies with the potential difference V.

- How will you obtain maximum capacitance from three given condensers?

- On inserting a dielectric between the plates of a capacitor, its capacitance is found to increase 5 times. What is the relative permittivity of the dielectric?

- Write the principle of Van de graff generator.

- Explain what is meant by dielectric polarization.

- Derive an expression for the energy stored in a parallel plate capacitor.

- A 600 pF capacitor is charged by a 200 V supply. It is then disconnected from the supply and is connected to another uncharged 600 pF capacitor. How much electrostatic energy is lost in this process?

- Three capacitors each of capacitance 9 pF are connected in series.

- What is the total capacitance of the combination?

- What is the potential difference across each capacitor if the combination is connected to a 120 V supply.

- Derive an expression for potential due to an electric dipole.

- Derive a relation between electric field and potential.

Ch 3 Current Electricity

- State the principle of working of a potentiometer.

- State two uses of potentiometer.

- State Kirchhoff’s rules.

- A cell of emf E and internal résistance r is connected across a variable resistor R. plot a graph showing the variation of terminal potential V with resistance R. predict from the graph the condition under which V becomes equal to E.

- What is the effect of temperature on the relaxation time of electrons in a metal?

- Find the value of carbon resistance when the sequence of bands marked on it, is brown, brown, black.

- Establish a relation between Emf and potential difference.

- Establish a relation between drift velocity and relaxation time of free electrons in a metallic conductor carrying a current.

- With the help of a circuit diagram describe a method to find the internal resistance of a cell using potentiometer.

- Find the current flowing through a copper wire of length 0.2 m, area of cross – section        1 mm2, when connected to a battery of 4V. Given that electron mobility as                         4.5 X 10-6 m2v-1s-1 and charge on electron 1.6 x 10-19C. The number density of electron in copper is 8.5 x 1028m-3